## Slide 1
LED Control using Capacitive Touch Sensor
UW-Stout Computer Engineering Program
CEE-345 Microprocessor System Design
Dylan Christopherson and Dr. Cheng Liu
Abstract
The goal for this project was to use the capacitive touch sensor to control the brightness on the onboard LED. Swiping from left to right would increase the brightness and swiping right to left would decrease the brightness. There would also be several push buttons to change the color of the LEDs.
Part List
Wiring Diagrams and Software
Code Snippets
The following parts were used for the construction of ….
Quantity | Part | Cost
1 | Freedom Board | $20
1 | Wires/breadboard | $5
1 | Tactile switches | $2
 | Total | $27
Final Project
Circuit Schematic/Project Structure
Capacitive Touch Sensor
The circuit schematic for this project was quite simple. The project required three tactile switches attached to the onboard pins. The capacitive touch sensor was onboard so the only configuration is software based.
This project was supported by Touch Sensing Software (TSS). A software pack put out by NXP Semiconductors. The project structure for the TSS is below.
Above are two of the most important snippets of code from the project. The top snippet is the main function for the project. Within this function, we call numerous functions to initialize different components involved in the project. These include the Init_5way_Switch() which initializes pins for the tactile switches. InitPorts() is the default Touch Sensing Software (TSS) initialization. PWM_init() initializes clock and sets up pulse width modulation. Within the main function in a infinite for loop, there is the Test_Switches() function. This function checks to see if any of the tactile switches are pressed, and if they are pressed, it calls the Control_RGB_LEDs() function. This uses the TSS function SET_LED_COLOR() and the TSS variable cASlider1.Position to set the color of the LED based on the position of the capacitive touch sensor.